## Slide 1
ARINC-717 Telemetry & Audio
over QUIC with DTN
Concept of Operations — High-Level Team Brief
180
Telemetry Signals
7
Architectural Layers
~80%
BW Reduction in Cruise
Classification: Internal Technical Brief | v2.0

## Slide 2
What Are We Solving?
✈ Aircraft generate massive data
180 telemetry signals + cockpit audio — all needing to reach the ground station reliably, even over intermittent satellite links.
📡 Links break. Data must not.
Satellite connectivity drops during manoeuvres, weather, and handoffs. Traditional TCP stalls and loses frames. We need something smarter.
⚡ Bandwidth is scarce & expensive
Transmitting everything, always, wastes cost. We need intelligent buffering — send only when it matters, burst when it's critical.
🔒 Every byte must be authenticated
In aviation, tampered telemetry is catastrophic. Every packet must carry cryptographic proof of origin and integrity before any station trusts it.
GOAL: Build a simulation that proves ARINC-717 + compressed audio can be reliably, securely transported over QUIC with intelligent store-and-forward — and measure every byte.

## Slide 3
7-Layer System Architecture
End-to-end flow from signal generation to verified ground reconstruction

## Slide 4
Layer 1 & 2 — Data Generation & Framing
TELEMETRY — 180 Signals
Signal types
Sine, ramp, step, noise, sawtooth
Quantisation
12-bit per sample (4096 levels)
Word rate
1024 words/sec (configurable: 64–1024)
Frame structure
4 subframes × 1 second each
Raw data rate
~1.5 KB/s before compression
Identity method
Position in frame = parameter ID
Ts table
Fast (Ts=1) to slow (Ts=8) per signal class
AUDIO — CVR Simulation
Source
Pre-recorded WAV/M4A or live mic
Chunk size
40ms per QUIC send (codec alignment)
Raw rate
~32 KB/s (16kHz 16-bit mono)
FLAC (lossless)
~16 KB/s — exact reconstruction
Opus (lossy)
~2 KB/s — speech-transparent CVR
Zstd+PCM
~14 KB/s — lossless middle ground
BW insight
Audio is 10× telemetry — the real cost
💡 Key insight: After compression, telemetry is ~0.3–0.6 KB/s. Audio at 16kbps (Opus) is ~2 KB/s. Total link budget for a full 3-hour flight is dominated by audio — telemetry is nearly free.

## Slide 5
Layer 3 — Compression & Cryptographic Security
Compression Algorithms
LZ4
Speed: ~1 GB/s
Ratio: Moderate
Best for: Real-time telemetry
Zstd L3
Speed: ~400 MB/s
Ratio: Good
Best for: Balanced frames
Zstd + Dict
Speed: Best ratio
Ratio: Excellent
Best for: Repetitive patterns
Bundle Packet Structure
4B
Magic Header
4B
Bundle ID
4B
Seq Number
8B
Timestamp (µs)
1B
Payload Type
1B
Compression Algo
4B
Payload Length
N
Compressed Payload
32B
HMAC-SHA256
64B
ECDSA-P256 Sig
🔐 HMAC-SHA256 (per packet)
Microseconds per packet. Symmetric key check — receiver immediately rejects forged or corrupted packets before processing. First line of defence.
🔐 ECDSA-P256 (per bundle)
Asymmetric signature over entire bundle. Proves origin — only the aircraft's private key can sign. Ground station verifies with public key. Non-repudiable.

## Slide 6
ACK Strategy — Design Decision
How the aircraft knows the ground station received each bundle — and what to do when it doesn't
Selected approach: QUIC Stream 2 ACK — lightweight receiver stats echoed back every bundle. Enables per-stream BW/latency accounting without DTN overhead.

## Slide 7
Layer 4 & 5 — DTN Store-and-Forward + QUIC Transport
DTN — Delay/Disruption Tolerant Networking
① Bundle written to SQLite queue with TTL
② Delivery attempted over QUIC Path A
③ On failure → retry Path B automatically
④ On path recovery → queued bundles drain
⑤ If all paths down → bundles persist on disk
⑥ Cap: 1000 bundles max, TTL discard warns operator
QUIC — Stream Assignment
Stream 0
Telemetry bundles
(reliable, ordered — priority lane)
Stream 1
Audio chunks
(reliable, ordered — 40ms chunks)
Stream 2
Server→Client ACKs
(BW stats + latency echo)
💡 QUIC multiplexing means audio backlog NEVER blocks telemetry — impossible in TCP. Critical for real-time safety data.
Failover: PING every 500ms. 3 consecutive fails → auto-switch to standby path. Live on dashboard.

## Slide 8
Transmission State Machine — Flight Phase Logic
Intelligent bandwidth control: only transmit what matters, when it matters
RESULT: For a 3-hour flight with one distress event, ~80% BW reduction vs always-on. Pre-event buffer (last 20 min) automatically burst-sent on distress detection.

## Slide 9
Post-Event Buffer Rules & Signal Timing (Ts)
Three cases for distress clearing + how signal sampling intervals (Ts) are assigned
Cruise entry gate: altitude_ft > 25,000 ft for 5 consecutive 4-second frames (20 seconds confirmation).

## Slide 10
Layer 7 — Ground Station Receiver & Verification
1
Receive QUIC streams
Split raw bytes into bundles by magic header (0xA717A717). Parallel stream buffers for telemetry vs audio.
2
ECDSA Verification
Reject entire bundle if signature invalid. Only aircraft private key can produce valid signature — tamper proof.
3
HMAC Per-Packet
Reject any packet with bad HMAC. Fast microsecond check. Corrupted packets never enter the pipeline.
4
Decompress
Use compression_algo field to select correct algorithm. No ambiguity — the header tells the receiver exactly how to unpack.
5
Unpack ARINC-717 Frame
Extract 180 signals from their fixed word-slot positions. Position IS the identity — no lookup table needed.
6
Reconstruct & Verify
Apply inverse 12-bit quantisation using [min, max] range. Compare RMS vs generated signal. Error ≤ quantisation noise floor.

## Slide 11
Expected Performance Numbers — Demo Dashboard Preview
Channel
Raw Rate
After Compression
HMAC+ECDSA
QUIC Headers
Telemetry (1024 w/s)
~1.5 KB/s
~0.3–0.6 KB/s
+0.4 KB/s
+0.1 KB/s
Audio — FLAC (lossless)
~32 KB/s
~12–16 KB/s
+0.1 KB/s
+0.1 KB/s
Audio — Opus (16kbps)
~32 KB/s
~2 KB/s
+0.1 KB/s
+0.1 KB/s
~0.5 KB/s
Telemetry after Zstd+Dict
~2 KB/s
Audio after Opus 16kbps
<5 ms
HMAC per packet overhead
~1 ms
ECDSA per bundle signing
Latency Measurement Method
◆ Each packet carries a microsecond send timestamp embedded in the header.
◆ Receiver echoes timestamp back on Stream 2 (ACK channel).
◆ Sender computes RTT = receive_time − send_time, and one-way = RTT/2.
◆ Separate per-stream latency tracked: telemetry vs audio independently.

## Slide 12
Module Architecture — Clean Separation of Concerns
Foundation
config.py
All tunable parameters. No magic numbers in code. Switch word rate, codec, paths — zero other changes.
Layer 1
signal_generator.py
180 signals → numpy arrays. Configurable types: sine, ramp, step, noise, sawtooth.
Layer 1
arinc717_ts.py
ARINC-717 framer with Ts-aware word slot assignment. 521/1024 words used. Compatible with base spec.
Intelligence
flight_phase.py
State machine: ENGINE_OFF→TAXI→TAKEOFF→CLIMB→CRUISE→DESCENT→LANDING. CruiseBuffer (20-min rolling). Distress detection on 15 signals.
Intelligence
tx_manager.py
Wires phase→TX policy. BUFFERED in cruise. DISTRESS fires burst. POST_EVENT collects 20 min then bursts. Returns to BUFFERED.
Layer 3
compressor.py
Unified interface: LZ4, Zstd, Zstd+Dict, FLAC, Opus. One compress(data, algo) call. Ground station mirrors exactly.
Layer 3
packet_builder.py
Binary pack: header + payload + HMAC-SHA256. Fixed byte layout. Ground station mirrors exactly.
Layer 3
bundle_signer.py
ECDSA-P256 sign/verify per bundle. Private key stays on aircraft node. Public key distributed to ground stations.
Layer 4
dtn_queue.py
SQLite persistent queue. TTL management. Dual-path failover. link_monitor pings every 500ms.
Layer 5
quic_client.py
aioquic aircraft sender. Three streams. RTT measurement. Per-stream BW tracker.
Layer 5
quic_server.py
aioquic ground station. Receives, verifies, decompresses, reconstructs. Mirrors client stats.
Observability
metrics.py + dashboard.py
Rolling 1-second BW window. Per-stream latency. Live terminal UI via rich. Shows every byte breakdown.

## Slide 13
Anticipated Questions & Design Decisions
Q: Why QUIC over TCP?
A: TCP head-of-line blocking stalls telemetry when audio bursts. QUIC streams are independent — telemetry always gets through.
Q: Why both HMAC and ECDSA?
A: HMAC = fast per-packet integrity check (microseconds). ECDSA = non-repudiable origin proof (proves aircraft signed it). Neither alone is sufficient.
Q: Why is the 20-min buffer circular, not flushed?
A: We always want the LAST 20 minutes up to the distress moment. A flush-every-20-min model would lose the minutes just before the event.
Q: What if both paths are down simultaneously?
A: Bundles queue to SQLite (disk) with TTL. When any path recovers, queue drains automatically. Dashboard shows queue depth live.
Q: Is 12-bit quantisation a problem for accuracy?
A: It's spec-compliant. Error = range/4096. We document the exact error bound and prove it's within spec at ground station via RMS comparison.
Q: Can we add more signals beyond 180?
A: Yes. config.py sets the count. The framer will allocate word slots automatically. 1024 words/subframe gives room for 503 additional slots.

## Slide 14
What We Are Building — And Why It Matters
A technically rigorous, fully measurable simulation that proves aviation telemetry
and cockpit audio can be transported reliably, securely, and intelligently over modern internet protocols.
Phase 1
Local demo — two QUIC servers on localhost. Kill Path A mid-demo to trigger visible failover. Dashboard live.
Phase 2
VirtualBox — two VMs with OpenConnect VPN as satellite link. Disconnect VPN mid-demo for real network failover.
Phase 3
Client demo — live dashboard showing per-channel BW, latency, compression ratio, ECDSA verification speed.
The simulation is the proof. Every number on the dashboard is real, measured, and defensible to a technical client.